VCR History up to Release 2.0k



                        PUMA:036/VCR2/HIST Revision 1.8



                           Mark Debbage                Mark Hill



                                    November 3, 1992



 This document lists changes to VCR since the second major release of the package (version
 2.0).

                                                                                                
  Base Version  Date     Modification                                                         

  VCR 2.0       27-6-91  Rebuilt release from product occam Toolset libraries             
                         Added files to regenerate vhostio.lib and vstream.lib             
                         Fixed PC driver program ncfcheck.exe and ncfcheck.arg          
                         Added miscellaneous text files to distribution disks               
                         Corrected single topology ncfcheck.c and ncfcheck.btl            
                1-7-91   Released as VCR 2.0a                                               
  VCR 2.0a      5-7-91   Corrected vdriver.c to permit networks with arbitrary host link  
                         Fixed vmove.c bug to mend DVCCreateChannelIns/Outs        
                16-7-91  Released as VCR 2.0b                                               
  VCR 2.0b      14-8-91  Corrected workspace misallocation in RPCs                      
                14-8-91  Released as VCR 2.0c                                               
  VCR 2.0c      25-6-91  Introduced deadlock-free links optimisations                      
                9-8-91   pdmake : added MSDOS internal command support             
                         pdmake : extended to large PC memory model                   
                21-9-91  Critical devices bug fixed                                         
                24-9-91  Removed knowledge of ports array from VCR                    
                         Added support for HPR hybrid links and configurations         
                2-10-91  Fixed exception buffer handling (corrupted 1 word of heap)      
                         MultiplePortGrab implementation fixed                         
                         Fixed pblock overflowing on valid pass value parameters by ref  
                3-10-91  Recompiled with patched libc.lib for full iserver functionality    
                         Released as VCR 2.0d                                               



                                               1





                                                                                                   
   
  Base Version  Date      Modification                                                          
   

  VCR 2.0d      25-10-91  ISERVER environment variable overrides path iserver in vdriver    
                          Truncated TCOFF files now detected correctly                      
                          Consistant handling of transputer error modes                       
                          Improved handling of virtual channels length mismatches            
                          Configurer alias checking disabled                                    
                          Source-less static makefile deleted from release                      
  
                27-10-91  Vestigial channels and configuration tables bugs in configurer fixed  
                29-10-91  Released as VCR 2.0e                                                 
   
  VCR 2.0e      2-12-91   Corrected routegen handling of check memory sizes                  
                          Added missing router and virtual transputer binaries                
                          Released as VCR 2.0f                                                 
   
  VCR 2.0f      26-2-92   Corrected reallocation for when code buffer filled                    
                1-4-92    Rationalization of vcr and svcr scripts                               
  
                          vdriver software gets dynamic bootables off $VCR/nets             
                          vdriver software gets .ncf files off NETSEARCH                     
                          svdriver software gets static bootables off NETSEARCH            
                          NETSEARCH order : local, $NETSEARCH entries, $VCR/nets    
                2-4-92    Added transprt.c to switch highest layer functionality               
                3-4-92    Released as VCR 2.0g                                                 
   
  VCR 2.0g      3-6-92    Added VPI and ParaPET support                                   
                          Loading of object code speeded-up                                   
                          routegen recognises n-cubes as deadlock-free                         
                          Minor changes to UPRI (internal packet routing interface)          
                5-6-92    Released as VCR 2.0h                                                 
   
  VCR 2.0h      19-6-92   Fixed a bug afflicting high priority ALTs                             
                29-6-92   Dynamically loaded actions run in user space                        
                2-7-92    Command-line switches to VCR can be in arbitrary order           
                6-7-92    Threads library improved to support low priority processes          
                15-7-92   UPRI exposes topology information on root processor               
                16-7-92   Added programs grid, torus, ring programs to release                
                21-7-92   routegen detects grid topologies and marks in ncf                    
                21-7-92   ROUTEGEN ARG environment variable holds default routegen options  
                21-7-92   Released as VCR 2.0i                                                 
   
  VCR 2.0i      28-7-92   Exposed topology correctly information through upri.lib             
                11-8-92   Fixed static loading command line options                           
                11-8-92   Fixed 2 by n grids in routegen                                        
                12-8-92   Released as VCR 2.0j                                                 
   
  VCR 2.0j      2-9-92    Fixed time-stamping mechanism in pdmake                          
                7-10-92   Added multiple-packet ORB routines: faster virtual channels        
                15-10-92  Bug removed from routegen topology recogniser                     
                15-10-92  Released as VCR 2.0k                                                 
   



                                                 2