[This is a summary of the slides presented by Roger Shepherd of INMOS
Ltd, Bristol, UK at the T9000 Systems Workshop given at the
University of Kent on the 14th and 15th of September 1992 presented
by the World occam and Transputer User Group (WoTUG) in association
with COMETT and the Software Environments for Parallel Computing
(SEPC) Initiative.

We have edited the slides slightly to make them more understandable
without the pictures and corrected a few typographical errors.

The information below is (C) Copyright 1992 INMOS Ltd, UK and is
presented with permission of INMOS.

The University of Kent at Canterbury and INMOS make no claims for the
validity of the information presented below and accepts no liability
for mistakes.

Transcribed by David Beckett (djb1@ukc.ac.uk) on 21st October 1992
]

[1]
		  T9000 Pipeline and Memory System

		Roger Shepherd - INMOS Ltd. Bristol


[2]

T9000 Goals

Very significantly faster than T805

Aim:	5x - 10x T805-20

Achieve via:	clock speed (2.5x)
		fast functional units
		architecture (2x - 4x)

		use pipelining
		   multiple instruction issue (superscalar)

Result:	200 MIPS, 25 MFLOP
	In practice we can manage > 50% of these figures


[3]

Review of Pipelining

Example: very simple 3 address register machine

Instruction		Pipeline stage	      c1  c2  c3
------------------	--------------------  ----------
I1:  r1 := r2 + r3	1. Read from reg (2)  I1  I2  I3
I2:  r2 := r3 + r4	2. ALU (1)		  I1  I2
I3:  r4 := r6 + r7	3. Write to reg (2)	      I1

1 instruction issued per cycle
3 instructions operating in parallel

"1 cycle per instruction"


[4]

Pipelining the Transputer Instruction Set

Can the transputer instruction set be pipelined?

{\em ldl} forms address; then accesses memory
{\em stl} forms address; then accesses memory

Sequences like {\em ldl;ldl} are common and could be pipelined


[5]

A Pipelined Transputer

		T805		x[i] := y[j]
		cycles

ldl	j	2		A M		[A=ALU, M=Memory, .=Skip]
ldl	y	2		  A M
wsub		2	(1)	    . A
ldnl	0	2		        A M
ldl	i	2			  A M
ldl	x	2			    A M
wsub		2 	(1)		      . A
stnl	0	2				  A M

		16	(14)    <----------------->
					10

This gives (only) 1.6x (1.4x) speed-up over T805.


[6]

Grouping: Pipeline Several Instructions at Once

Consider the previous example:

	ldl j; ldl y; wsub 0; ldnl 0
	ldl i; ldl x; wsub 0; stnl 0

This is effectively

	load  ( Mem[Wptr + 4*y] + 4*Mem[Wptr + 4*j] )
	store ( Mem[Wptr + 4*x] + 4*Mem[Wptr + 4*i] )

This is what the T9000 does. (2 cycles for the above)


[7]

Beware Memory Accesses!

Note that executing

	ldl j; ldl y; wsub 0; ldnl 0
	ldl i; ldl x; wsub 0; stnl 0

in 2 cycles requires access to

	4 locals, 2 non-locals and 2 words of instructions

	in 2 cycles - 3 words per cycle!


[8]

T9000 - Processor Pipeline

The processor operates by forming "groups" of instructions

	eg ldl; ldnl; ldl; ldnl; add

and executing these on a pipeline

Fetch &  Local    Address  Main     ALU/FPU  Write
Group    Cache             Cache
-------  -------  -------  -------  ------   ------
|     |  |     |->|     |->|     |->|     |  |    |
|     |->|-----|  |-----|  |-|---|  |     |->|  | |
|     |  |     |->|     |->| |   |->|     |  |  | |
-------  -------  -------  -----|-  -------  ---|--
   |                         |  |               |
   ^  Groups                 ^  ^               V
   |                         |  |               |
  Read                    Read  Read          Write


[9]

Use of Pipeline by Instructions (1)


-----------------------------------------------------
		local	address	main	alu	write
-----------------------------------------------------
ldc		L
ldlp		L
ldl (hit)	L
ldnl			A	M
ldnlp			A
eqc		L			A
stnl			A			W
-----------------------------------------------------
wsub / bsub		A
sum / add				A
-----------------------------------------------------


[10]

Use of Pipeline by Instructions (2)

Some instructions are implemented in terms of others

stl		ldlp; stnl

adc		ldc; add

ldl (conflict)	ldnlp; ldnl
ldl (miss)	ldnlp; ldnl; copyAtoLocalCache


[11]

Use of Pipeline by Instructions (3)

-----------------------------------------------------
		local	address	main	alu	write
-----------------------------------------------------
eqc		L			A

j		X
cj (local)		X		A
cj (other)				X

eqc 0; cj (local)	A		A
eqc 0; cj (other)			A

The instruction targetted by the jump can execute 3 cycles after the
jump (X) has been taken.


[12]

T9000 - Use of Pipeline (1)

[Consider the following example:]

typedef struct {float real, im;} complex;

complex *x, *y, *z;

x->real = (y->real * z->real) - (y->im * z->im);


[13]

T9000 - Use of Pipeline (2)

[This maps to the following code and groups as follows:]

---------------------------------------------------------
ldl		1	-- y	GROUP 1 - 4 instructions
fpldnlsn				  6 bytes
ldl		0	-- z
fpldnlmulsn
---------------------------------------------------------
ldl		1	-- y	GROUP 2 - 6 instructions
ldnlp		1		 	  8 bytes
fpldnlsn
ldl		0	-- z
ldnlp		1
fpldnlmulsn
---------------------------------------------------------
fpsub				GROUP 3 - 3 instructions
ldl		2	-- x		  5 bytes
fpstnlsn
---------------------------------------------------------
...


[14]

T9000 - Use of Pipeline (3)

G1: ldl fpldnlsn ldl fpldnlmulsn
G2: ldl ldnlp fpldnlsn ldl ldnlp fpldnlmulsn
G3: fpsub ldl fpstnlsn


	Step 1		Step 2		Step 3
------------------------------------------------------------------
L	G1: ldl,ldl	G2: ldl,ldl	G3: ldl
A			G1:		G2: ldnlp, ldnlp
N-L					G1: fpldnlsn, fpldnlsnmul
FPU
W
------------------------------------------------------------------
	1 cycle		1 cycle		1 cycle


[15]

T9000 - Use of Pipeline (4)

	Step 4		Step 5		Step 6		Step 7
---------------------------------------------------------------------
L
A	G3:
N-L	G2: fpldnlsn,	G3:
	    fpldnlsnmul
FPU	G1: fpldnlsnmul	G2: fpldnlsnmul	G3: fpsub
W			G1:		G2:		G3: fpstnlsn
---------------------------------------------------------------------
	2 cycles	2 cycles	2 cycles	1 cycle

6 cycles per 3 groups
         per 13 instructions gives > 2 instructions/cycle
			     gives about 108 MIPS
	 per 3 fp operations gives 25 MFLOPS


[16]

Question:

"Does the hardware grouper imply that good compilers need not be
expensive and that programmers will not have to craft careful
assembler inserts to sustain high efficiency in the pipeline?"


[17]

Answer:

The compiler must be targetted at the T9000:

Issues: grouping and addressing/arithmetic

	char *p, c;

	c = *(p+1);

Either

  ldl p; ldc 1; bsub; lb	1 group - 1 cycle

OR
  ldl p; adc 1; bsub; lb	2 groups - 3 cycles [since adc=ldc+add ?]

[Note: discussion with the audience concluded that the main thing to
ensure was that you generate address-manipluating instructions (e.g.
ldc) to compute addresses, NOT arithmetic instructions (e.g. adc) to
compute addresses (even though the arithmetic instructions may use
less bytes of code-space).  This is really all the transputer
compiler writer nees to appreciate about the T9000 pipeline
architecture!]


[18]

T9000 - Memory Hierarchy

	-------   -------------   -----------
	| VCP |   | SCHEDULER |   |   CPU   |
	-------   -------------   -----------
	   |            |         |   |    |
	   |            |         ^   v    ^
	   |            |      ----------- |
	   |            |      |Workspace| |
	   |            |      |Cache    | |
	   |            |      ----------- |
	   |            |         |   |    |
	   |            |         ^   v    |
	   |            |         |   |    |
	-------------------------------------
	|          MAIN   CACHE             |
	-------------------------------------
	                |
	-------------------------------------
	|       EXTERNAL  MEMORY            |
	-------------------------------------


[19]

T9000 - Memory Access Capabilities of Subsystems

CPU       - up to 4 accesses per cycle
VCP       - up to 3 accesses per cycle
Scheduler - up to 1 access per cycle


[20]

T9000 - Multibanked Memory System

(Physical) address space is divided into 4 banks:

	bank 0 is selected by bits 5 and 4 being 00
	bank 1 is selected by bits 5 and 4 being 01
	bank 2 is selected by bits 5 and 4 being 10
	bank 3 is selected by bits 5 and 4 being 11

Each bank contains 4Kbytes of cache memory

All banks may operate concurrently.


[21]

T9000 - Memory Architecture Diagram

                  |          |          |          |
-----------|------o----------o----------o----------o-
|CPU       |------o----------o----------o----------o-
|          |------o----------o----------o----------o-
-----------|------o----------o----------o----------o-
                  |          |          |          |
-----------|      |          |          |          |
|Scheduler |------o----------o----------o----------o-
-----------|      |          |          |          |
                  |          |          |          |
-----------|------o----------o----------o----------o-
|VCP       |------o----------o----------o----------o-
-----------|------o----------o----------o----------o-
                  |          |          |          |
-----------|      |          |          |          |
|External  |------o----------o----------o----------o-
|Memory    |      |          |          |          |
-----------|      |          |          |          |
              ---------  ---------  ---------  ---------
              |Cache  |  |Cache  |  |Cache  |  |Cache  |
              |Memory |  |Memory |  |Memory |  |Memory |
              ---------  ---------  ---------  ---------  
               Bank 0     Bank 1     Bank 2     Bank 3


[22]

"Devices" and "Memory"

Devices		affected by accesses, e.g. csr of UART
		order of access to different addresses matters
		spurious reads matter
		cannot be cached

Memory		returns last value written to a given address
		order of access to different addresses does not matter
		spurious reads do not matter
		can be cached


[23]

T9000 [Memory Access] Behaviour

The T9000 accesses memory out of order

e.g. ldl x; ldl y; ldnl z; add performs the accesses as PAR(x,y); z

The T9000 accesses memory speculatively

IF
  w = 1
    x := y
  TRUE
    x := z

ldl w; eqc 1; cl L; ldl y; stl z; .L

ldl y will occur even if the conditional jump is taken! [because of
the grouping in the pipeline]


[24]

T9000 Device Accesses

Normal loads and stores are, therefore, unsuitable for accessing
devices.

The T9000 provides special load and store instructions to access
devices
	- they execute in order
	- there is no speculative execution

[Note: the compiler writer must be aware of when she is dealing with
memory and when she is dealing with a device.  This is easy for occam
compiler writers (since the language distinguishes between these
things) ... but difficult for C!]

The T9000 EMI [External Memory Interface] allows banks to be marked
as "device"
	- allows access from links
	- allows access from processor "device" instructions only
	- allows no speculative access
	- is uncached


[25]

T9000 Cache Coherency

The T9000's internal memory is kept coherent.

There is no hardware implementation of cache coherency for external
memory.

Options: uncached memory
	 software control via {\em flush dirty cache address}
			      {\em flush dirty cache line}
			      {\em invalidate cache address}
			      {\em invalidate cache line}


[26]

T9000 Cache [Summary]

4K bytes per block - 16K total

Each bank - fully associative (256-way)
	  - 4 words per line (16 bytes)
	  - write back
	  - allocate on write miss

The cache may be used as - 100% cache
			 -  50% cache and 50% RAM
			 - 100% RAM

When used as RAM, the addresses are programmable.


[27]

Question [to the audience]

"How much arithmetic per external store access needs to be done to
enable the cache mechanisms to keep the processor running at full
speed?  How does the cache hardware affect context switch times and
interrupt response latency?  How do we decide whether to use full,
half or zero on-chip cache?"


[A discussion followed to which the answer was mainly along the lines
of "...it depends!"]