Network communications
 
The use of INMOS links for directly connecting transputers has already been
described. The new link protocol not only simplifies the use of links
between processors but also provides hardware support for routing messages
across a network.
 
-----------------------------------------------------------------

Message routing
 
The VCP (virtual channel processor) on the sending IMS T9000 packetises
messages to be sent over a link and adds a header to each packet to
identify the destination process. At the receiving end, the VCP uses the
header to send the data in each packet to the intended process. These
headers can also be used for routing packets through a communication system
connecting a number of IMS T9000s together. This extends the idea of
multiple channels on a single hardware link to multiple channels through a
communications system; a communications channel can be established between
any two processes even if they are running on transputers that are not
directly connected. The header still just specifies the destination of the
packet; the programmer does not need to know how to route that message to
its destination.
 
Advantages for the programmer
-----------------------------
 
The ability to have channels between any two processes in a network  has a
number of significant advantages for the programmer. It simplifies the
description of multiprocessor systems by separating the hardware
architecture from the software configuration. The programmer doesn't need
to be concerned with the details of placing channels on links or routing
messages through the network. This removes a lot of the problems with
placing of processes on processors - the decision now can be made just on
the basis of the resources (memory size, etc.) available on each processor
without worrying about the available connectivity.
 
The programming model for networks of IMS T9000 transputers is unchanged
>from that for the first generation of transputers. There is, however,
greater flexibility in configuring software. An important feature is that
the hardware and software configurations, and therefore their descriptions,
can be kept completely independent. The same hardware, and the same
description of that hardware, can be used for many different programs.
 
Routers
-------
 
The routing components in a network can be separated from the processing
elements. Messages can be passed from one processor, through any number of
routing devices, to the destination processor. This creates a temporary
path through the routing system for that message so, from the programmers
point of view, there still appears to be a single channel directly
connecting a process on one transputer with a process on another.
 
<picture>
 
Figure 7.1  -- A routing system
 
As a packet arrives on a link, the destination address must be inspected
before the outgoing link can be determined. The time before the output link
can be determined is therefore proportional to the address length. Further,
the address itself must be transmitted through the network and consumes
network bandwidth. It is therefore important that this address be as short
as possible, both to minimise latency and maximise bandwidth.
 
The router needs to arbitrate between packets which arrive at the  same
time and have to be sent out of the same link. Ideally, it should start to
output the packet as soon as possible; i.e. immediately after the output
link is determined, provided that the link is not already in use by another
packet. This keeps the latency through the network small, in contrast to a
typical packet switching network which uses a `store and forward' algorithm
in which each packet is read into a buffer, the address information is
decoded and then the packet is sent out. The delay that would be introduced
by this is unacceptable in a transputer network. Also the amount of
buffering needed would make a VLSI implementation of a large routing switch
impractical.
 
Separating routers and processors
---------------------------------
 
There are a number of advantages to keeping the communications devices  and
processing elements separate in a system. Processors can be directly
connected where appropriate, which avoids the silicon costs and extra
routing delays in a small system that doesn't need to use the routers.
Also, the design of the routing devices and processing elements can be
optimised for their different roles. For example, the routing component can
have a larger number of links than would be possible if the two devices
were integrated, because the processor already needs a large number of pins
for the memory interface and other functions. Having a routing device with
many links means that large network with a small number of routers can be
built, hence minimizing cost and latency and maximizing bandwidth. If
messages had to flow through the processor, it would increase the pin
count, power consumption and packaging costs. This approach also allows the
construction of scaleable architectures where the communications throughput
and processing power can be balanced.
 
Parallel networks
-----------------
 
Because the new link architecture allows all the virtual channels  of a
transputer to use a single link, complete, system-wide connectivity can be
provided by connecting just one link from each transputer to the routing
network. This means that the IMS T9000, with its four links, can be
connected to several different networks. This can be exploited in a number
of ways. For example, two or more networks can be used in parallel to
increase bandwidth, to provide a general purpose communications network and
an independent monitoring/debugging network, or as a `user' network
running in parallel with a physically separate `system' network.
 
-----------------------------------------------------------------

The IMS C104
 
An important benefit of the IMS T9000's serial links is that it is easy to
implement a full crossbar in VLSI, even with a large number of links. The
use of a crossbar allows packets to be passing through all links at the
same time, making the best possible use of the available bandwidth.
 
If the routing logic can be kept simple it can be provided for all  the
input links in the router. This avoids the need to share the hardware,
which would cause extra delays when several packets arrive at the same
time. It is also desirable to avoid the need for the large number of packet
buffers commonly used in routing systems. The use of small buffers and
simple routing hardware allows a single VLSI chip to provide efficient
routing between a large number of links.
 
Wormhole routing
----------------
 
The IMS C104 (figure 7.2) is one of a family of compatible communications
support devices for the IMS T9000. It includes a full 32 x 32 non-blocking
crossbar switch, enabling messages to be routed from any of its links to
any other link. In order to minimise latency, the switch uses `wormhole
routing' - the connection through the crossbar is set up as soon as the
header has been read. The header and the rest of the packet can start being