Other communications devices
 
To complete the IMS T9000 family, a full range of communications products
are planned. These will provide the ability to interface transputers to a
range of devices and technologies.
 
-----------------------------------------------------------------
Mixing transputer types: the IMS C100
 
The first of these devices is the IMS C100. This allows an IMS T9000 to
communicate with a first generation transputer. The two transputer families
have different electrical characteristics and data protocol. The IMS C100
converts between the four wire DS links of the IMS T9000 and the two wire
OS links of the earlier transputers.
 
The other conversion done by the IMS C100 is between the IMS T9000 control
links and the Reset, Error and Analyse signals used to control the IMS T805
and similar device.
 
The IMS C100 provides an inter-networking solution for transputers,
allowing transputer systems to be constructed using the optimum mix of
devices. The IMS C100 has four modes of operation to enable:
 
** A single IMS T9000 to work in a network of first generation transputers.
 
** An existing transputer system to control a sub-system of IMS T9000s.
 
** An IMS T9000 network to interface to a network of first generation
transputers.
 
** A first generation transputer to emulate an IMS T9000.
 
<picture>
 
Figure 8.1  -- IMS C100 used with an IMS T9000
 
The IMS C100 converts both data and control protocols between the two
transputer types and is intended to be used in conjunction with software
running on the attached transputers.
 
<picture>
 
Figure 8.2  -- IMS C100 used with a first generation transputer
 
-----------------------------------------------------------------

Interfacing to peripherals and host systems
 
To complete the family of communications devices, a range of interface
devices are being designed. These will convert between the serial link
format and a parallel interface, for example. The first of these devices
will interface to a microprocessor bus. This will allow the IMS T9000 to
communicate with non-transputer systems.